## Slide 1: Maury 2640D Slide Screw Tuner
Ansys HFSS Simulation Dimensions

## Slide 2
The Simulation includes three parameters.
  D1 -> Depth of Tuner Probe 1
  D2 -> Depth of Tuner Probe 2
  Lateral -> Lateral Movement Length (Common for Both Probes).
Datasheet: 1.2

## Slide 3: Aluminium Slabs
127.35 mm
(length)
40.6 mm
(width)
9.3 mm
(height)

## Slide 4: Top View
127.35 mm
40.6 mm
9 mm
Aluminium Slab
Slab Holder
23.55 mm
14 mm
Inner Conductor

## Slide 5: Side View
24.2 mm
9.3 mm
5.6 mm
Inner Conductor
Air Dielectric
1.275 mm
1.275 mm

## Slide 6: Inner Conductor
There is no explicit mentioning of the material of the inner conductor in the Datasheet of the tuner.
But the tuner mentions a connector type of 7mm.
It is explicitly mentioned in the datasheet of the 7mm connector, that the inner conductor is of BeCu with Gold plating.
The same has been used in the simulation also.
Link: 1.1
BeCu
3.05 mm
0.05 mm
Gold

## Slide 7: Tuner Probe 1
The Tuner probe material is also assumed to BeCu, as the purpose of the tuner is to affect the EM waves in the inner conductor.
20.6 mm
Top View
16.6 mm
Side View
2 mm
5.5 mm
20.6 mm

## Slide 8: Tuner Probe 2
The Tuner probe material is also assumed to BeCu, as the purpose of the tuner is to affect the EM waves in the inner conductor.
20.6 mm
6 mm
Left Side View
2 mm
5.5 mm
20.6 mm
Top View
10.6 mm
12.7 mm
5.9 mm

## Slide 9: Probe Lateral Movement
9.3 mm
7 mm
Total Length of Aluminium Slab = 127.35mm
Movement Restriction on both sides= 14 mm (7 on each side)
Effective Movement Length = 113.35 mm
TP1
TP2
TP1
TP2
7 mm

## Slide 10: Probe Depth Movement
Minimum Depth
1.15 mm
6.1 mm
Maximum Depth
Note: This movement parameters are applicable for both Tuner Probe 1 & Tuner Probe 2